INSTRUCTION MANUAL

Please read this manual thoroughly before use, and keep it handy for future reference.

Table of Contents

Chapter 1 — Introduction	1

1.1 Features	1

1.2 System Requirements	2

Chapter 2 — Installation	3

2.1 Installation	3

2.2 Upgrade	3

Chapter 3 – System Setup	4

3.1 System Setup	5

3.2 System Setup – Device / Layout / Sequence	6

3.3 System Setup – Device	12

3.4 System Setup – Schedule	17

3.5 System Setup – Disk	19

3.6 System Setup – Layout	19

3.7 System Setup – Emap	20

3.8 System Setup – Sequence	22

Chapter 4 – Event Setup	23

4.1 Event Setup – Device	23

4.2 Event Setup – System	25

4.3 Event Setup – SMTP	26

4.4 Event Setup – Relay Out	27

Chapter 5 – User Setup	28

5.1 User Setup – User	28

5.2 User Setup – Authority	29

Chapter 6 – Option Setup	30

6.1 Option Setup – System	31

6.2 Option Setup – Video	34

6.3 Option Setup – OSD	35

Chapter 7 – Main/Sub Menu	36

7.1 Main Menu	36

7.2 Sub Menu	38

7.3 Tray Menu	39

Chapter 8 - Joystick	40

8.1 Joystick Connect / Disconnect	40

8.2 Joystick Functions	41

Chapter 9 – Device Tree	42

9.1 Device	42

9.2 Layout	45

9.3 Channel Sequence	45

9.4 Layout Sequence	46

9.5 Favorite	46

Chapter 10 – Live View	48

10.1 Live View	48

10.2 PTZ Control	50

10.3 Live Toolbar	52

10.4 Event List	56

Chapter 11 – Local Playback	57

11.1 Date and Time Search	57

11.2 Playback Controls	58

11.3 Event Search	62

11.4 Favorite Search (Bookmark)	63

11.5 Event Report	64

11.6 Local File Playback	65

11.7 Playback Toolbar	67

Chapter 12 – Device Playback	69

12.1 Device playback	70

12.2 Playback Controls	70

12.3 Event Search	70

12.4 favorite search	71

12.5 Text-In Search	71

12.6 Device Playback Toolbar	73

Chapter 13 – Emap View	75

13.1 Emap View	75

13.2 Emap Toolbar	76

Chapter 14 – Event View	78

14.1 Event View	78

14.2 Event Toolbar	78

14.3 Event List	79

Chapter 15 – Status View	80

15.1 Status Toolbar	80

15.2 Device Status	81

15.3 System Status	83

15.4 Device System/Event Logs	84

Chapter 16 – Clip Viewer	85

16.1 Export Footage	85

16.2 Open Local File	86

16.3 Playback Control	86

16.4 Event View	87

16.5 Split Mode()	87

16.6 Snapshot	87

16.7 Previous Split Group / Next Split Group	87

Chapter 17 - Easy Install	88

17.1 Easy Install procedure	88

Chapter 18 - DDVRLS Setup	90

18.1 NVR setup	91

18.2 Titanium client setup	93

Appendix A - Specification	94

Appendix B - Toolbars	96

Appendix C - Directories	99

Appendix D - Keys	100

Appendix E - Messages and Logs	101

Appendix F – Hard Disk Format	103

List of Figures

Figure 1 Login	4

Figure 2 Add/Modify/Remove Computer	4

Figure 3 System Setup Menu	5

Figure 4 Setup Login	5

Figure 5 System Setup	5

Figure 6 Add Device	7

Figure 7 Add Layout	8

Figure 8 Layout	9

Figure 9 Sequence	10

Figure 10 Device Searching	10

Figure 11 System Setup - Discovery	12

Figure 12 Device Type Search	13

Figure 13 IP Filtered Device Discovery	13

Figure 14 Device Menu	13

Figure 15 Remote Setup	14

Figure 16 System Setup - Weekly Schedule	17

Figure 17 System Setup - Special Day Schedule	18

Figure 18 Disk	19

Figure 19 Emap	20

Figure 20 User Image Size	21

Figure 21 Event Setup	23

Figure 22 Event Setup - Device	23

Figure 23 Event Setup - System	25

Figure 24 Event Setup - SMTP	26

Figure 25 Event Setup - Relay Out	27

Figure 26 User Setup	28

Figure 27 Setup User	28

Figure 28 Option Setup	30

Figure 29 Option Setup - System	31

Figure 30 Option Setup - Video	34

Figure 31 Option Setup - OSD	35

Figure 32 Main Menu/Sub Menu	36

Figure 33 Login dialog - option	36

Figure 34 Main menu (Free Version)	37

Figure 35 Sub Menu	38

Figure 36 Tray Menu	39

Figure 37 Joystick	40

Figure 38 Device Tree	42

Figure 39 Device Menu	43

Figure 40 Device Properties	43

Figure 41 Recording Property	44

Figure 42 NVR Device Menu	44

Figure 43 Layout Item	45

Figure 44 Channel Sequence Item	45

Figure 45 Layout Sequence Item	46

Figure 46 Favorite	46

Figure 47 Add User Layout	47

Figure 48 Modify User Layout	47

Figure 49 Favorite – Default Setting	47

Figure 50 Main	48

Figure 51 Set Event Channel	49

Figure 52 Window Tab Show/Hide	50

Figure 53 PTZ Control Panel	50

Figure 54 PTZ in Screen	51

Figure 55 Zoom Control of PTZ in Screen	51

Figure 56 Live View Toolbar	52

Figure 57 Live Screen Title and Toolbar	53

Figure 58 Event List	56

Figure 59 Playback View	57

Figure 60 Playback Calendar Control	58

Figure 61 Time Combo-box	59

Figure 62 Remote Export	59

Figure 63 Insert Favorite	60

Figure 64 Play Speed Control	61

Figure 65 Time Overlapped Playing	62

Figure 66 Event Search	62

Figure 67 Favorite Search	63

Figure 68 Event Report	64

Figure 69 Local File Playback	65

Figure 70 Local Export	66

Figure 71 Time Bar	66

Figure 72 Local Playback Toolbar	67

Figure 73 Playback View Split Control	67

Figure 74 Playback Screen Title and Toolbar	68

Figure 75 Device Playback	70

Figure 76 Text-In Search	71

Figure 77 Text-In View	72

Figure 78 Text-In Filter	72

Figure 79 Device Playback Toolbar	73

Figure 80 Screen Title and Toolbar	73

Figure 81 Emap View	75

Figure 82 Emap Toolbar	76

Figure 83 Event View	78

Figure 84 Status View	80

Figure 85 Status Toolbar	80

Figure 86 Device Status Table	82

Figure 87 Split Status	82

Figure 88 System Status	83

Figure 89 System Log Filter	83

Figure 90 Log Search Result	84

Figure 91 Device System/Event Log	84

Figure 92 Clip Viewer	85

Figure 93 Export Footage	85

Figure 94 Event View	87

Figure 95 Easy Install	88

Figure 96 Easy Install – Setup	88

Figure 97 Easy Install – Camera Selection	89

Figure 98 Easy Install – Recording disk and schedule setup	89

Figure 99 DDVRLS Setup	90

Figure 100 Dashboard Setup Registration	91

Figure 101 DDVRLS Registration	91

Figure 102 Dashboard Setup Login	92

Figure 103 Remote Watch / Search	92

Figure 104 DDVRLS setup	93

List of Tables

Table 1 System Requirements	2

Table 2 Device Type	7

Table 3 Device Tree Buttons	11

Table 4 Discovery List Item Icon	12

Table 5 Discovery Tools	12

Table 6 Maintenance	15

Table 7 Color vs. Meaning in the Time Table	17

Table 8 Emap Control Buttons	22

Table 9 Device Event Operations	24

Table 10 Live Update Check	33

Table 11 Device Status	42

Table 12 Sequence Control Tools and Operations	49

Table 13 Joystick Buttons and PTZ Operations	52

Table 14 View Toolbar	52

Table 15 Toolbar Position	53

Table 16 Calendar Controls	58

Table 17 Play Controls	61

Table 18 Time Jump	61

Table 14 Function Support for NRV Type	69

Table 19 Emap Zoom Controls	77

Table 20 Emap Zoom Controls	77

Table 21 Status Toolbar Buttons	80

Table 22 Device Status Table	81

Table 23 Device Status Table Text Colors	81

Table 24 Playback Control	86

Chapter 1 — Introduction

## 1.1 Features

This is extremely powerful and intelligent surveillance software. This guide explains how to install the software as well as how to configure and use.

( 7 monitors for live, playback and status

( 4 live monitors as Live1, Live2, Event and Emap

( Up to 64 splits per live monitor displaying

( Up to 16 splits for playback displaying

( Various layout modes

( Channel and layout sequence mode

( Event channel/layout view

( Multi-layered Emap view

( 64 channels recording

( NVR support

( Unlimited recording disk size and configurable multiple disk and device assignment

( Various recording modes (manual, weekly schedule, special day schedule, event and event-relay recording)

( Various search modes (time lapse, event and favorite searching) and playback controls

( Remote network device configuration

( Easy PTZ (PTZ panel and in-screen PTZ) and alarm controls

( Useful view and toolbars for easy control (Digital zoom, Audio, Freeze, Manual-Recording, Microphone, Split controls and etc.)

( User and authority management

( Keyword searching

( Automatic device discovery

( Easy check system and device status and logs

( Automatic/manual check updating and live update

( Event notification, searching and reporting

## 1.2 System Requirements

The following are the minimum system requirements for this software

Table 1 System Requirements

| Operating System | Microsoft® Windows® XP Professional (32 bit or 64 bit), Windows Vista™ Enterprise/Ultimate (32 bit or 64 bit), Windows 7 Professional/Enterprise /Ultimate (32 bit or 64 bit) * Windows 7 recommended |
| --- | --- |
| CPU | Intel® Core™2 Quad processors or higher (Core™ i7 processor recommended) |
| RAM | Minimum 1 GB (4 GB or more recommended) |
| Network | Ethernet (1 Gbit recommended) |
| Graphics Adaptor | PCI-Express, minimum 1024 x 768, 16 bit colors (256 MB or more isolated VGA memory, 1920 x 1080, 32 bit colors recommended) |
| Hard Disk Type | E-IDE, PATA, SATA (7200 RPM or faster), Network drives |
| Hard Disk Space | Minimum 1 GB free disk space available for software Minimum 4 GB free disk space available for each recording disk |
| Joysticks | USB PC Compatible Joysticks |
| DirectX | DirectX end-user runtimes (June 2010 and later) http://www.microsoft.com/download/en/details.aspx?id=8109 |

This software runs as a 32 bit service and application with the 64 bit operating systems.

Chapter 2 — Installation

## 2.1 Installation

Before installation, shut down and remove any previous installed versions.

Do not install this on a network drives, otherwise the software MAY not work properly.

Procedure

1. Insert the software CD/DVD; then click the installation link.

Alternatively, if you are installing the file version, run the installation file from the location.

Depending on your security settings, you MAY get one or more security warnings. If that is the case, click the Run button.

2. When the installation wizard starts, click ‘next’ to continue.

3. Read and accept the EULA (End User License Agreement), then click ‘next’.

4. Select ‘typical installation’ and follow the instructions.

5. Click Finish to complete the installation.

## 2.2 Upgrade

With the live updating function, the software may be upgraded at your convenience. The old configuration will be automatically converted to the new format. The previous configuration will be applied to the updated software.

You don’t need to remove the current version of the software manually. The installation of the new version will remove the current version automatically.

Do not use the old version of software with the new configuration. The new configuration MAY not work with the old version of software.

Back up your current configuration

When you install the new version, it will take the configuration from your old version and convert it to the new format of configuration automatically. However, we recommend that you make regular backups of your configuration.

Procedure

1. Create a folder to backup the configuration on a network drive or removable media device.

2. Open ‘My Computer’ with the explorer and C:\ProgramData\NCTitanium\ (case of Windows 7).

3. Copy the files and folders to your backup folder.

Chapter 3 – System Setup

After installation, access the software by double-clicking the NC-Titanium desktop shortcut. Alternatively, use Window’s start menu: Start > All Programs > NCTitanium > NCTitanium.

Figure 1 Login

Enter the User ID and Password when prompted by the Login dialog. The default User ID and Password are “admin” and “admin”. Local computer is the default computer, and user can add/modify/remove computer by clicking  button if needed.

Figure 2 Add/Modify/Remove Computer

## 3.1 System Setup

After logging into the software, click the main menu in the title bar and select the System Setup menu.

Figure 3 System Setup Menu

Figure 4 Setup Login

The System Setup requires administrator level authority. Enter the default User ID and Password in the Setup Login dialog after the first installation.

Figure 5 System Setup

There are 3 categories: ① main setup menu (SYSTEM, MODULE, EVENT, USER, and OPTION). The ② device tree is to manage the device group, the device and layout, and the channel and layout sequence. The ③ configuration property tabs contain menus and configurations for the main setup menu.

## 3.2 System Setup – Device / Layout / Sequence

The System Setup is to configure devices, layouts, channel and layout sequences and recording schedule and policy.

The device tree is to manage the device group, device, layout, channel and layout sequence.

### 3.2.1 Device Group/Device

1) Add device group

① Select the Device root item from the tree.

② Click the right mouse button.

③ Select the Add Group menu from the popup menu.

④ Enter the group name.

2) Rename device group

① Select the device group from the tree to rename it.

② Click the right mouse button.

③ Select the Rename Group menu from the popup menu.

④ Enter the new group name.

* Press the F2 key to rename the tree item

3) Remove device group

① Select the device group item(s) to remove from the tree.

② Click the right mouse button.

③ Select the Remove Group menu from the popup menu.

④ Confirm removing group from the message.

* When a group is removed, all devices in the group will also be removed. It affects the layout, channel and layout sequence.

* The recording data will remain even if the device is removed from the configuration.

* Press the Delete key to remove the selected item(s) from the tree.

4) Add devices from the Discovery tab

① Create a group to add a device.

② Select devices (streams) in the Discovery tab and drag into a group to add.

5) Add devices manually

① Create or select a group to add device.

② Click the right mouse button.

③ Select Add Device menu.

④ Edit the device properties (name, address, port, user ID, password and others).

Table 2 Device Type

| Device Type | Description |
| --- | --- |
| IP Camera Type A | Hitron IP Camera |
| IP Camera Type B | Hitron IP Camera |
| IP Camera Type C-1 | Hitron IP Camera |
| IP Camera Type C-2 | Hitron IP Camera |
| NVR A | Hitron NVR (not type B) |
| ONVIF Device | ONVIF Camera with ONVIF |
| IP Camera supported RTSP | Camera with RTSP support |
| NVR B | Jupiter Plus NVR Series / Venus NVR Series |

⑤ Click the ‘Check Verify’ button.

⑥ If it connected successfully, click the ‘Save’ button.

Figure 6 Add Device

### 3.2.2 Layout

1) Add layout

① Select the Layout root item from the tree.

② Click the right mouse button.

③ Select the Add Layout menu from the popup menu.

④ Enter the layout name and description and select the layout mode in the Add Layout dialog.

Figure 7 Add Layout

2) Rename layout

① Select the layout item to rename from the tree.

② Click the right mouse button.

③ Select the Rename Layout menu from the popup menu.

④ Enter the new layout name.

* Press the F2 key to rename the tree item.

3) Remove layout

① Select the layout item(s) to remove from the tree.

② Click the right mouse button.

③ Select the Remove Layout menu from the popup menu.

④ Confirm removing layout from the message.

* Press the Delete key to remove the tree item(s).

4) Design layout

① Select the Layout tab and select a layout name in the combo-box.

Figure 8 Layout

② Select a group/(a) device(s) from the tree and drag it into the layout position to set up the device name.

③ If you want to delete a device from the layout, select the device from the layout and click the right mouse button.

④ Select the Remove option from the popup menu.

* Press the Delete key to remove the device from the layout in the tree or Layout tab.

### 3.2.3 Channel/Layout Sequence

1) Add channel/layout sequence

① Select the Channel Sequence / Layout Sequence root item from the tree.

② Click the right mouse button.

③ Select the Add Channel Sequence / Add Layout Sequence menu from the popup menu.

④ Enter the sequence name.

2) Rename channel/layout sequence

① Select the sequence item to rename from the tree.

② Click the right mouse button.

③ Select the Rename Channel Sequence / Rename Layout Sequence menu from the popup menu.

④ Enter the new sequence name.

* Press the F2 key to rename the tree item.

3) Remove channel/layout sequence

① Select the sequence item(s) to remove from the tree.

② Click the right mouse button.

③ Select the Remove Channel Sequence / Remove Layout Sequence menu from the popup menu.

④ Confirm removing sequence from the message.

* Press the Delete key to remove the tree item(s).

4) Design channel / layout sequence

① Select the Sequence tab and select a channel / layout sequence name in the combo-box.

Figure 9 Sequence

② Select a group/(a) device(s)/(a) layout(s) from the tree and drag into the sequence to set up.

③ Set up the dwell time to display device/layout.

④ If you want to delete a device/layout from the sequence, select the device/layout from the sequence and click the right mouse button.

⑤ Select the Remove menu option from the pop-up menu.

### 3.2.4 Device searching

There is an edit-box which is for searching device item.

Figure 10 Device Searching

It searches and selects the matching device by item name, IP address, MAC address, firmware version, URL, model name, profile name. If a layout item has a description or image path that matches with any searching text, it will automatically be selected.

Table 3 Device Tree Buttons

| Device Tree Buttons | Operations |
| --- | --- |
|  | Searching device |
|  | Clear searching text |
|  | Add user dynamic layout |
|  | Remove user dynamic layout |

## 3.3 System Setup – Device

This option supports automatic device discovery and setup.

### 3.3.1 Discovery

This feature tries to contact the devices which are attached to the network. It MAY take a few minutes to complete.

Figure 11 System Setup - Discovery

1) Connection status

The Discovery tab shows the devices which are connected to the network by model name, device name, MAC address, IP address and firmware version. Each icon on the item list displays the results of its connection test.

Table 4 Discovery List Item Icon

| Connection Test Results | Results Key |
| --- | --- |
|  | It’s not available to connect |
|  | It’s connected |
|  | It’s locked and needs ID and password |

2) Discovery tools

The device discovering process is able to be controlled by the below buttons.

Table 5 Discovery Tools

| Buttons | Operations |
| --- | --- |
|  | Begin device discovery |
|  | Halt device discovery |
|  | Refresh list and restart device discovery |

3) Device Type Search

- Select device type for searcg in combo-box.

- When the device type is selected, corresponding devices in the network are searched and a list of devices are shown below.

Figure 12 Device Type Search

4) IP filtered device discovery

① Check the IP filter enable button.

② Enter the specific IP address ranges to discover the devices in the network.

③ Click the Apply button. Then the devices are discovered in the specified network address ranges.

Figure 13 IP Filtered Device Discovery

### 3.3.2 Device setup

There are some useful tools to setup the devices.

① Select the device item(s) from the list.

② Click the right mouse button.

③ Select the Remote Setup menu.

④ Setup the device configurations. The remote setup dialogs are different depending on the device model.

* Please refer to the device manual in the setup menu.

* If the Quick View feature is enabled (located in the configuration menu) for the device, you MAY be able to see the image simultaneously while the configuration is being applied.

Figure 14 Device Menu

Figure 15 Remote Setup

### 3.3.3 Quick view

This is to see the video/image stream from the device instantly.

① Select the device item(s) from the list.

② Click the right mouse button.

③ Select the Quick View menu.

④ Select the video/image stream profile and connection type from the combo-boxes.

⑤ The Stop/Play button is to stop and resume the video/image stream.

### 3.3.4 Assign IP

This is to assign the IP address for the selected device.

① Select the device item(s) from the list.

② Click the right mouse button.

③ Select the Assign IP menu and click the Ok button.

④ The result will automatically assign the selected device with a new IP address.

* After changing the IP address, click the Refresh button. Otherwise, visually, the IP address won’t reflect the changes.

### 3.3.5 Maintenance

There are 3 maintenance functions, Restart, Reset and Factory Default. The Reset function MAY be operated differently depending on the device model.

Table 6 Maintenance

| Restart | Restarts the device without any changes |
| --- | --- |
| Reset | Resets the configuration except some specific values (ex. network) The client may need to be restarted for the changes to take place. |
| Factory Default | Resets all configurations to the default factory settings. The client may need to be restarted for the changes to take place. |

* After the Factory Default, the device MAY need some time to recalibrate and connect.

### 3.3.6 Upgrade firmware

① Select the device item(s) from the list to upgrade.

② Click the right mouse button.

③ Select the Upgrade Firmware menu.

④ Select the firmware file from the file open dialog.

⑤ The upgrading progress will be shown and it MAY take time to be updated and restarting the system.

* Please check the image file for the device before upgrading. Upgrading the wrong image file MAY cause the device to malfunction.

### 3.3.7 Login

This is to set the device login ID and password.

① Select the device item(s) from the list.

② Click the right mouse button.

③ Select the Login menu.

④ Enter the login ID and password.

* The default login ID and password are “admin” and “admin”.

* If the icon of the device shows this symbol, it represents that the login ID and password are not matched with the device settings.

### 3.3.8 Device Web Page

This function connects to camera web page. If the camera is un-reachable, this function does not work. If the web page does not shows, please check the network configuration of the Windows system. (IP address, Subnet Mask, Gateway)

① Select the device item(s) from the list.

② Click the right mouse button.

③ Select the Device Web Page menu.

### 3.3.9 Emergency Firmware Upgrade

In the case of specific failures, for example halting while upgrading firmware or upgrading wrong image file, the device MAY be halted. If the network function of the device works properly, it MAY be updated this way.

① Select the device item(s) from the list.

② Click the right mouse button.

③ Select the Emergency Firmware Upgrade menu.

④ Click the OPEN button and select the correct image file for the device.

⑤ Click the UPDATE button and check the STATUS.

* In the case of specific network device failure, the device MAY not be discovered this way. The Emergency Firmware Upgrade is only useful when the network function of the device works properly.

## 3.4 System Setup – Schedule

The Schedule tab is to configure weekly/specific event based items.

### 3.4.1 Weekly recording schedule

This is to set up weekly-hour based recording schedule.

Figure 16 System Setup - Weekly Schedule

- Select the Schedule tab.

- Select a device to set up recording schedule.

- Click the Weekly button.

- Select the time table by dragging.

- Click the right mouse button.

- Select the New Time Schedule or New Event Schedule menu.

- If you want to clear the schedule then select the Clear menu

Table 7 Color vs. Meaning in the Time Table

| Color of the table | Meaning |
| --- | --- |
|  | No schedule |
|  | Event recording schedule |
|  | Time recording schedule |
|  | Adaptive Time/Event schedule (Normal : key frame only, Event : full-frame recording) |
|  | Selected time cell |

- Set up the recording properties (Audio, Pre/Post-Recording).

- If you want to apply the same schedule to the other devices, click the ‘Apply to’ button and select the device(s)/group(s).

* The Pre/Post-Recording values are only for the event recording schedule.

* If the streams are from the same device then the recording properties are applied to all streams.

* If the Audio is enabled, the audio stream from the device will be recorded with video.

### 3.4.2 Special day recording schedule

This is to set up special day hour based recording schedule.

Figure 17 System Setup - Special Day Schedule

① Click the Special Day button.

② Click the Add button to add the special day recording schedule.

③ Double-click the date from the calendar.

④ Set the recording schedule to the desired period.

⑤ If you want to remove the special day schedule, click the Remove button.

⑥ Check the Enable Special Day Recording box to enable it.

⑦ If you want to apply the same schedule to other devices, click the ‘Apply to’ button and select the device(s)/group(s).

⑧ Set up the recording properties (Audio, Pre/Post-Recording)

⑨ If you want to apply the same special day recording schedule to the others, click ‘Apply to’ button and select the device(s)/group(s).

* The special day recording priority is higher than the weekly schedule.

## 3.5 System Setup – Disk

### 3.5.1 Disk

The Disk tab is to configure the recording hard disk drives and recording policy.

Figure 18 Disk

1) Disk assignment

① Select the Disk tab.

② Select the device(s) from the tree and drag into the disk tree to assign recordings.

③ Set up the recording disk properties.

* The streams which are from the same devices will be assigned automatically to the same disk drives.

* To utilize the disk performance, the streams are assigned to the separate disk drives.

* The Retention Time is to preserve the time of the recording data if the disks are available.

* The Reserved Disk Size is the recording disk size for the selected disk drive.

## 3.6 System Setup – Layout

This is to design the Layout. The Layout is used to view the layout as well as the Emap. Please refer the ‘3.2.2 Layout for adding, renaming and removing layout’.

## 3.7 System Setup – Emap

This is to design Emap using the layout.

Figure 19 Emap

### 3.7.1 Load background image

① Click the Emap tab.

② Select the Layout item from the combo-box to design Emap.

③ Click the Load Emap Background Image button () and select the image. Available image formats are JPG, PNG and BMP.

* The recommended Emap background image size is 800 x 600. If the image size is too big, it MAY take a little time to operate with it. If the image size is too small, E-map design and operation MAY not run optimally.

* The loaded images (background image, user device, user sensor and user link images) are copied to the specific directory automatically. If you remove the background images manually from that directory, it MAY lead to problems in operating Emap functions.

### 3.7.2 Device design

① Select the device(s) and drag it (them) to your target location.

② Select a device and click the right mouse button.

③ The Rename is to set a specific name only for Emap.

④ The Open Live View option serves to open a popup window displaying the live stream.

⑤ The Change Image option serves to change the device icon.

⑥ If you want to use your own device image, click the Load Emap User Device Image button () and select the image file. Available image formats are JPG, PNG and BMP. And the height of image MUST be 84 pixels and the width MUST be multiple of 28 pixels.

The top image represents normal, middle does selected, and the bottom is for event notification.

* Please refer the sample images which are installed.

C:\ProgramData\NCTitanium\MonitoringService\Emap\ (case of Windows 7)

Figure 20 User Image Size

⑦ Select user device image from the Change User Image menu.

### 3.7.3 Sensor/Link design

① Click right mouse button on the back ground image.

② Select the Insert Sensor/Insert Link menu.

③ Select the device group > device > sensor or manual trigger item.

④ If you want to rename it, click right mouse button and select Rename.

⑤ If you want to the change image, click right mouse button and select Change Image.

⑥ If you want to use your own sensor/link image, click the Load Emap User Sensor Image button ()/ Load Emap User Link Image (). And click right mouse button and select the Change User Image. The user sensor and link images MUST be the same condition of width and height as above.

* Double-click the link, then the Emap changes to the selected link. You can make a layered Emap with the link.

* The Manual Trigger is only available if the device supports it. Before designing the manual trigger, please check the device specification and setup for that operation.

### 3.7.4 Emap controls

There are some Emap control buttons.

Table 8 Emap Control Buttons

| Emap Control Buttons | Operations |
| --- | --- |
|  | Wide 16:9 Split Mode (5,7,12,14,20,24,30) |
|  | Standard 4:3 Split Mode (1,4,6,8,9,10,13,16,17,21,25,28,33,34,36,40,49,64) |
|  | Full Screen |
|  | Snapshot |
|  | Freeze |
|  | Manual Record Off/On |
|  | Speaker Mute On/Off |
|  | Microphone Mute On/Off |
|  | Emap Scale Up |
|  | Emap Scale Dawn |
|  | Emap Reposition |
|  | Previous Emap |
|  | next Emap |
|  | Emap Close |
|  | Previous Split Group |
|  | Next Split Group |
|  | Disconnect All Devices |
|  | Set/Reset Event Channel |
|  | Sequence Mode Status/Off |
|  | Sequence Timer On/Off |
|  | Previous Sequence View Point |
|  | Next Sequence View Point |
|  | Sequence View Point List |

## 3.8 System Setup – Sequence

This is to set up the channel/layout sequence. Please refer the ‘3.2.3 sequence for adding, renaming and removing sequence’.

Chapter 4 – Event Setup

This is to set up event operations. The device events are dependent on the device model. For example, some devices MAY support only motion and alarm event. And others MAY support manual trigger, on boot, video loss, network loss as well as motion and alarm. Please check the device model and setup before configuring this.

Select the EVENT menu.

Figure 21 Event Setup

## 4.1 Event Setup – Device

This is to set up the event operation. When an event happens on the device, the configured operations (view channel/layout, sound, execute external application, and recording, etc.,) would be worked. And the Event Relay is to relay event to other devices.

Figure 22 Event Setup - Device

### 4.1.1 Event operations

① Select the Device tab.

② Select a device from the device tree.

③ Select an event type to set up from the combo-box.

④ Enable/Disable the selected event operation from the list.

⑤ Set up the event operations.

⑥ If you want to apply the same operations to other devices, select the Apply to button and select device(s)/group(s).

Table 9 Device Event Operations

| Event Operations | Options | Settings |
| --- | --- | --- |
| Enable | Yes/No | Enable/Disable the event operations |
| View Channel | Dwell Time | Amount of time to display the event channel |
|  | Live View | What view to show the event channel on Live1, Live2, Emap and All. |
| View Layout | Dwell Time | Amount of time to show the layout |
|  | Layout | What layout to show in the Event view |
| Sound | Enable | Enable/Disable the sound |
|  | File | Select the sound file, otherwise the default sounds will be automatically be initiated |
| Event Popup | Enable | Enable/Disable Event Popup |
|  | Dwell Time | Amount of time to show Event Popup |
| Record | Dwell Time | Event Recording independent on schedule |
| Preset | Preset ID | In the case of PTZ, move the preset |
| Manual Trigger | Trigger ID | If it supports manual trigger, it will trigger |
| Event Relay | Relay Out List | Select the Relay Out |

* The Record operation in the device event list only affects the recording schedule. For example, if there is a device which is configured that there is no recording (time/event) schedule from 9:00 AM to 10:00 AM. If an event which operation is recording, is happened during that time, it would be recorded as configured with above setting value.

* The Relay Out has the similar configurations of the device event. Please do not configure relay chains. (For example, a manual trigger of device A relays a manual trigger of device B. And manual trigger of device B relays manual trigger of device A. It makes relay chain continuously. It MAY cause endless event operations)

* The View Channel option needs event channel setting on the Live1, Live2 and Emap. If there is no event channel setting on them, it will not work.

* The Dwell Time values of the View Channel and View Layout have a minimum time out of 5 sec. If another event occurs, the view channel and layout MAY be preemptive even though the value is over 5 seconds.

## 4.2 Event Setup – System

This is to set up the system event operations as like Disk Fault, Disk Full and System Update events.

Figure 23 Event Setup - System

### 4.2.1 System event operations

① Select the System tab.

② Select a system event type to setup from the combo-box.

③ Enable/Disable the selected event operation from the list.

④ Check the SMTP receiver to send the event information mail.

⑤ Enable/Disable the Sound.

⑥ Select the sound file.

* The mail receivers are able to be configured in the SMTP tab. Please refer the ‘4.3 Event Setup – SMTP’.

## 4.3 Event Setup – SMTP

This is to set up the SMTP settings. When an event is occurs in the system, this will send emails to the configured instructions.

Figure 24 Event Setup - SMTP

### 4.3.1 SMTP setting

① Select the SMTP tab.

② Check/Uncheck the Enable SMTP.

③ The Sender is the email address of the system administrator.

④ The Interval is the mailing interval. The range is from 1 min to 24 hours.

⑤ The Aggregate Events is the count of the events to send.

* If the Interval is 1 minute, this would check event to send every minute. If the Interval is 24 hours, this would check event to send in a day and send it.

* If the Aggregate Events value is 50, this would not send email until 50 events happened.

* If the Interval is 1 hour and the Aggregate Events value is 50, this would check and send email in every hour. And if the number of events is over 50, this would send an email every hour.

### 4.3.2 SMTP server information

① Check/Uncheck the Use Mail Server.

② Fill the mail server address and port to the list.

③ Fill the Login Name and Password of the mail server address.

④ Select the Login Method.

* Without SMTP server information, there MAY be a failure in the email transmission.

### 4.3.3 Receiver and SMTP Test

The maximum mailing list is 10. If you want to test mailing, enter the receiver address and click the Test button.

## 4.4 Event Setup – Relay Out

This is to set up event relay out. After setting this, each relay out item is selectable in the Device tab. Please refer the ‘4.1 Event Setup – Device’ to assign the event relay out to the device event.

Figure 25 Event Setup - Relay Out

### 4.4.1 Event relay out

① Select the Relay Out tab.

② Click the Add button and enter the relay out name.

③ Select the device from the device tree and drag it into the below of the list.

④ Set up the Record, Manual Trigger and Preset.

* The Record is the recording dwell time.

* The Manual Trigger is dependant on the device model.

* The Preset is only available for the PTZ device.

* Before setting up the Manual Trigger and Preset, please check the device model and settings.

* If an event is assigned with relay out, the event will occur as it is configured with Manual Triggering and PTZ preset movement.

* Do not create a chained relay out, for instance an event from device A triggers the device B and the event which was triggered by B triggers the device A again and again.

### 4.4.2 Remove relay out

Select the relay out item from the list. Click the Remove button.

### 4.4.3 Rename relay out

Double-click the relay out item from the list and enter new name of it.

Chapter 5 – User Setup

This supports multi-users. Each user is able to be assigned the device, layout and sequences. This describes how to configure users and authorities. The default administrator user ID is “admin” and the password is “admin”. After installation, please change the password of the “admin” for safety. The “admin” is not able to be removed.

Figure 26 User Setup

Save the configuration otherwise the changes will not be applied. The old configuration would be saved in the specific directory. The old configurations MAY be useful to get technical support. The old configuration saving directory is C:\Program Data\NCTitanium\MonitoringService\Logs, case of Windows 7. This keeps maximum 20 old configurations.

## 5.1 User Setup – User

Select the User menu.

### 5.1.1 Add user

① Select the User tab.

② Click the Add button.

Figure 27 Setup User

③ Select the Group. A member of the Administrator group is capable to setup the system and access all devices, layouts and sequences. A member of the User group is not able to enter the system setup.

④ If you want to add one user, check/uncheck the Assign All Devices, Layouts, Sequences. If it is not checked, an administrator SHOULD reassign devices, layouts and sequences.

⑤ Enter the Password and Confirm password fields. And Click the Ok button.

### 5.1.2 Modify user

① Select a user to modify from the list.

② Double-click it or click the Modify button.

③ Modify the user information and click OK to save.

### 5.1.3 Remove user

Select a user(s) to remove from the list and click the Remove button.

## 5.2 User Setup – Authority

This is to assign the devices, layouts and sequences to users.

### 5.2.1 Set up authorities

① Select a user from the combo-box.

② Select a device(s) from the device tree and drag it (them) into the Device list.

③ Select a layout(s) from the device tree and drag it (them) into the Layout list.

④ Select a sequence(s) from the device tree and drag it (them) into the Sequence lists.

* If a layout is assigned to a user, all devices which belong to that layout are assigned automatically.

* If a sequence is assigned to a user, all devices which belong to that sequence are assigned automatically.

⑤ If you want to remove a device(s), layout(s) or sequence(s), select and click right mouse button.

⑥ Select the Remove menu.

* If a user is a member of the Administrator group or is already assigned to all devices, layouts and sequences, then the user is not listed in the combo-box.

Chapter 6 – Option Setup

This is to set up various options of system, video and OSD (On Screen Display).

Select the OPTION menu.

Figure 28 Option Setup

## 6.1 Option Setup – System

This is to configure language, automatic login/logout mode and system live update checking and logs.

Select the System tab.

Figure 29 Option Setup - System

### 6.1.1 Language

This software supports multi-language functions and the language preference is user-configurable.

1) User configurable language

You can export the language items from the software in run-time. After editing the exported language file and place it under the specific directory. Then the language is ready to be used. The procedures are below.

① Select the System tab.

② Click the Export button in the Language.

③ Select the file to export.

④ Open the exported file (.ini) with text editor. (ex, Notepad)

⑤ Edit the right side strings of the equal mark.

* Do not change the number.

[StringTable] 100=OLE initialization failed. Make sure that the OLE libraries are the correct version. 101=Login 102=Logout [number]=[string]

* If the system is updated, the language file MAY not be compatible with the updated version.

⑥ Place the user language file in the Languages directory under the system using.

(C:\Program Data\NCTitanium\MonitroingService\Languages\  - case of Windows 7)

⑦ Click the Reload button.

⑧ Select the language file name from the Language combo-box.

⑨ Click the Apply button. The selected language will be applied.

* Some strings MAY not be matched with the window dialog. In that case, please re-define the strings.

* Some of strings would be applied after restarting the software.

2) Multi-languages

The software MAY include some languages. You can select the language from the combo-box and Click the Apply button. The selected language would be applied.

### 6.1.2 Access Right

This is to set up the automatic login and logout.

1) Automatic login

To login automatically with the specific user, check the Enable automatic login check-box and select the user to be applied. Otherwise, uncheck it.

2) Automatic logout

To logout automatically without asking for user confirmation, check the Enable automatic logout without checking user information. Otherwise, uncheck it.

### 6.1.3 Abnormal termination

There is a possibility that if the software client is terminated without the correct procedure, the next time you start the client, you MAY receive a message of abnormal termination. If this is checked, even though there is any abnormal termination, the last user who logged in will remain logged in and the last Live1, Live2 views will be restored automatically (without message checking).

### 6.1.4 System Update

This is an automatic check for software updates. Checking will be done automatically, but updating software needs user confirmation. This is to configure updating server and method.

① Check the Automatic Check and select the time.

② Enter the update server URL (for example, http://192.168.0.1/liveupdate/nctitanium)

③ If the update server requires a user ID and password for accessing, check the user ID/password to login the update server.

④ Click the Check button to access the server.

Table 10 Live Update Check

| After Starting Up | Whenever any administrator level user logs in |
| --- | --- |
| Before Closing | Before the software closing |
| All | After Starting Up and Before Closing |

* Please consult the updating server with the network administrator or software installer.

### 6.1.5 Retention Logs

This option determines how long the logs will be kept in the system. The default value is 6 months. The logs older than 6 months would be removed, and the removed logs are not recoverable.

### 6.1.6 Camera Default Setting

This option determines default protocol for camera connection among UDP, TCP, or HTTP.

### 6.1.7 BackUp

1) Export

This option stores information of device, storage, layout, channel display sequence, layout sequence, and favorite. When you click Export button, “Save As” dialog box will appear. Determine path and file name, and click Save button, then Export operation will start.

2) Import

This option recalls setup information from an exported file. This operation will delete current setting and replace with information in the file, so a warning window shows up and if you click Yes, the Import operation continues. At Open dialog box, select appropriate file and click Open button, then Import operation will start.

## 6.2 Option Setup – Video

This is to configure video displaying mode and snapshot.

Select the Video tab.

Figure 30 Option Setup - Video

### 6.2.1 Display

The performance of this software is very dependant on the VGA (video graphic adaptors) which are installed. Some systems use shared memory with VGA and system. In that case, the performance MAY not be better than the isolated memory system. And some VGA don’t support specific displaying modes. In that case the default mode is YV12 and faster. Before changing this option, please check the VGA specification which is installed.

### 6.2.2 Video snapshot

It is to configure automatic snapshot and directory to save the snapshot images.

Click the Find button and select the directory to save snapshot images. The snapshot image format is one of BMP, JPEG and PNG. The File name is used to generate the image file name with prefix. The Sequential numbering is the option when the file is already existed.

If it is checked the [Automatically save snapshot when you click the snapshot button] check-box, the snapshot images would be saved automatically without asking dialog.

### 6.2.3 Video stream

It is to configure stream information of NVR type B. There are three stream types, stream 1, stream 2, and auto. If you select stream 1 or 2, then the selected stream of designated camera is displayed on live view screen.  If you select auto, stream 1 will be displayed for quad or single mode, and stream 2 will be displayed otherwise.

## 6.3 Option Setup – OSD

This is to configure date and time format and screen title text and color.

Select the OSD tab.

Figure 31 Option Setup - OSD

### 6.3.1 Date & time format

Select the Date and time format from the combo-boxes.

### 6.3.2 OSD

Select the Item and the Font option. The screen example shows the selected options at the same time.

Chapter 7 – Main/Sub Menu

After installation, access the software by double-clicking the NC-Titanium desktop shortcut. Alternatively, use Window’s start menu: Start > All Programs > NC-Titanium > NC-Titanium.

There are main menu, sub menu and tray menu.

## 7.1 Main Menu

The main menu is for login/logout, system setup and others. And the button color shows the service status. Click the Main menu button (: logged out, : logged in)

Figure 32 Main Menu/Sub Menu

### 7.1.1 Login

After starting the program, if the automatic user login is not set, the Login dialog will pop up. Select the computer and enter the user ID and password to login. Click the Main menu and select the Login menu to show the Login dialog.

If you want to add/remove the computer, click ‘option’ button on login dialog.

Figure 33 Login dialog - option

* If you want to configure automatic login/logout, please refer the ‘6.1.2 Authority’.

Figure 34 Main menu (Free Version)

If the user login is successful, the Main menu will display a connected status icon ().

### 7.1.2 Logout

When you want to log out from the program not closing it, you can select the Logout from the main menu. If the automatic logout is not set, the Logout dialog would be popped up. Enter the user ID and password to logout.

If the user logged out successfully, the Main menu would be changed disconnected status ().

### 7.1.3 System Setup

This is to enter the system setup menu. Entering the system setup menu is available only to the Administrator level users. Click the System Setup menu and enter the user ID and password in the Setup Login dialog.

* Please refer the ‘3.1 System Setup’.

### 7.1.4 Lock/Unlock

The Lock is to lock all user access except main/sub menu. To unlock, click the Main menu and select the Unlock and enter the locked user’s password in the Unlock dialog.

### 7.1.5 About

The About is to check the software version and EULA (End User License Agreement) document.

If the Administrator level user is logged in, the Update Check button is available.

To use the Update Check manually, the live update server information MUST be needed.

* If you want to live update, please refer the ‘6.1.4 Update check’.

### 7.1.6 Exit

If you want to close this program, click the Exit from the Main menu. Or click the close button () in the right side of title bar. Depending on the system configuration, the User Logout dialog MAY be popped up.

## 7.2 Sub Menu

The Sub menu is to open snapshot directory and manage recording service. Click the Sub menu button ().

Figure 35 Sub Menu

### 7.2.1 Open snapshot directory

Click the Open snapshot directory from the Sub menu, windows explorer would open the configured snapshot saving directory.

### 7.2.2 Open Video Directory

Click the Open video directory from the Sub menu, windows explorer would open the configured clip video saving directory.

### 7.2.3 Backup Status

Click Backup Status of Sub Menu opens backup status list.

### 7.2.4 Start recording/stop recording

The Start Recording and the Stop Recording are visible only the current user is an administrator level user. The recording service is started or stopped by manually with this. Even if the recording service would be stopped, the relaying live stream would not be stopped.

## 7.3 Tray Menu

Click the right mouse button on the Tray icon.

Figure 36 Tray Menu

### 7.4.1 Start recording/stop recording

The Start Recording and Stop Recording are available only for the administrator level users. Refer the ‘7.2.2 Start recording/stop recording’.

Chapter 8 - Joystick

This chapter explains the setup and usage of Hitron USB keyboard. When user connects Hitron USB Keyboard to PC for the first time, the Windows Update automatically installs the necessary drivers.

[Automatic installation is for Windows 7 and later versions.]

When user connects the Hitron joystick for the first time, user needs to input password. [Default password: 1111]

* User needs to install manually for Windows XP and earlier versions.

* When the driver installation process is finished, please restart PC.

* This software does not support keys related to Local Playback / Device Playback.

## 8.1 Joystick Connect / Disconnect

User can connect or disconnect Joystick by clicking joystick icon().

Figure 37 Joystick

- Connect

Click the joystick icon and the dialog box opens as in Figure 36. Select each items user want to change and click Connect button.

- Disconnect

Click the joystick icon and the dialog box opens as in Figure 36. Click Connect button.

## 8.2 Joystick Functions

- Channel Selection

Press channel number and then press CAM button.

- Full Screen Mode

Press MAIN button. If user presses MAIN button in full screen mode, the full screen mode is released.

- Channel Scale Up

Press GROUP button then the selected channel scales up to fit in window. If user presses GROUP button in scale up state, the channel scale up is released.

- Up/Down/Left/Right/Diagonal Movement

Move joystick in desired direction.

- Magnify/Shrink

Press Magnify/Shrink button.

- Iris Control

Press Iris Open/Close button.

- Focus Control

Press Focus Near/Far button.

- Preset

Press preset number while pressing PRST button.

- Scan

Press Scan number while pressing SCAN button.

(10) Pattern

Press Pattern number while pressing PATTERN button.

(11) Tour

Press Tour number while pressing TOUR button.

Chapter 9 – Device Tree

This chapter describes the device tree. The root items of the device tree are the Device, Layout, Channel Sequence and Layout Sequence.

The Device has groups and devices. The Layout has layouts and devices. The Channel Sequence has sequences and devices. The Layout Sequence has sequences and layouts.

Figure 38 Device Tree

## 9.1 Device

The Device item shows the number of device items. It has device groups and devices.

### 9.1.1 Device status

The device icon represents connection, recording and event status.

Table 11 Device Status

| Tree Icon | Device Status |
| --- | --- |
|  | The network between device and the recording service is disconnected. |
|  | The network between device and the recording service is connected. |
|  | Recording. |
|  | An event is happened. |
|  | Recording and an event is happened. |

### 9.1.2 Device menu

Select a device under the device group. Click the right mouse button.

Figure 39 Device Menu

1) Remote setup

Select the Remote Setup menu. Then the remote setup menu window would be popped. It is the same with the ‘3.3.2 Device Setup’.

2) Property

Select the Property menu. Then the Device Properties window would be popped up.

Figure 40 Device Properties

It shows the device information (Group Name, Device Type, Name, Address, Port, and User ID/Password) and connection information (Type, RTSP configuration and others).

Click the Live button and then you can control PTZ, Menu and OSD control.

* If there is limitation of the connections in the device, it MAY not be connected.

3) Recording property

Select the Recording property menu. Then the recording property window would be popped up. You can check the recording schedule. For more information of the recording schedule, please refer the ‘3.4 System Setup – Schedule’.

Figure 41 Recording Property

4) Open device web page

Select the Open device web page menu. Then internet web page of the device would be opened.

### 9.1.3 Multi-select devices

The device tree supports multi-select with Ctrl and Shift keys. The multi-selection supports only the same level items, for example devices in the same group.

### 9.1.4 NVR Device menu

Select a NVR device under the device group. Click the right mouse button.

Figure 42 NVR Device Menu

Remote Setup

Select the ‘Remote Setup’ menu. Then the NVR remote setup window would be popped. Please refer to the NVR manual.

Setup Wizard

Select the ‘Setup Wizard’ menu. Then the NVR setup wizard window would be popped. Please refer to the NVR manual

## 9.2 Layout

The Layout item icon represents the split mode (number of screens).

Figure 43 Layout Item

The Layout item has device items and each item shows the screen id.

## 9.3 Channel Sequence

The channel sequence item has device items. And the order of the devices is the sequence order.

Figure 44 Channel Sequence Item

## 9.4 Layout Sequence

The layout sequence item has layout items. And the order of the layouts is the sequence order.

Figure 45 Layout Sequence Item

## 9.5 Favorite

Favorite item contains Layout items. Each layout item saves and restores user defined window layout.

* Support

- Multi-Monitor

- Window Layout / Camera Assignment Save and Restore

- FishEye Position Layout is not supported : will be supported

* Version

- NC-Titanium, TitaniumNVR 1.2.0.8 or later

Figure 46 Favorite

- Add Favorite

- User makes window layout first.

- Select Favorite item and click the right mouse button.

- Select Add User Layout menu.

- Type in a name in Add User Layout dialog box and click Add button.

Figure 47 Add User Layout

- Restore Window Layout

Double-click the desired layout.

- Remove Window Layout

Select the layout user wants to remove, click right mouse button, and select Delete in the pop-up menu.

- Modify Window Layout

Select the layout user wants to modify, click right mouse button, and select Modify in the pop-up menu. Type the layout name and press Add.

Figure 48 Modify User Layout

- Default Setting

When user starts NC-Titanium and log-in, the program restores default window layout. To setup default window layout, select desired layout and click right mouse button. Select default setting in the pop-up menu. When a layout is set to default, the color of the layout becomes red.

Figure 49 Favorite – Default Setting

Chapter 10 – Live View

This chapter describes how to operate the live view mode. There are 4 live view modes (Live1, Live2, Emap and Event).

The main user interface consists of ① Device tree panel, ② PTZ and Event control panel and ③ View tabs (Live1, Live2, Playback, Emap, Event and Status)

If you click the left mouse button on the screen tab and drag it into the other monitor, the screen view would be shown as full screen mode.

Figure 50 Main

## 10.1 Live View

There are 4 live view modes (Live1, Live2, Emap and Event). This describes briefly about the live1 and live2. Each view mode supports a maximum of 36 channels.

### 10.1.1 Live view by device/group/layout

① Select a Live view tab.

② Select a device/group/layout item in the device tree.

③ Drag it into the view screen. If you drag a layout, then the split mode will be changed automatically as it is configured.

### 10.1.2 Channel/Layout sequence view

① Select a Live view tab

② Select a channel/layout sequence item in the device tree.

③ Drag it into the view screen.

④ The remaining dwell time of view will be displayed in the title bar. And the sequence tools are enabled in the toolbar of the view.

Table 12 Sequence Control Tools and Operations

| Sequence Control Tools | Operations |
| --- | --- |
|  | Enable/Disable sequence mode status. Click it, disable sequence mode. |
|  | Continuous sequence timer status. Click it; the sequence timer will pause. |
|  | Pause sequence timer status. Click it, the sequence timer will continue. |
|  | Change to the previous sequence view point. |
|  | Change to the next sequence view point |
|  | Show the sequence view point list. Select a view point from the list, change to the selected view point. |

### 10.1.3 Event view

① Select a Live view tab.

② Select a screen and click the Set/Reset Event Channel. If an event is occurred and the event operation of that is configured that the Channel View is enabled, the channel would be shown in the Event Channel.

③ The channel screen is set as the Event Channel, then the background of the screen is highlighted.

④ The Event channel is to be set only one per screen view (Live1, Live2, Emap).

* Please refer the ‘4.1 Event Setup-Device’ to setup event channel view.

Figure 51 Set Event Channel

### 10.1.4 Window tab Show/Hide

① Click right mouse button on desired window tab.

② A pop-up menu will be displayed to setup window tab.

③ You can select/unselect desired window tab to show/hide.

Figure 52 Window Tab Show/Hide

## 10.2 PTZ Control

This supports 3-ways PTZ control, by the PTZ panel, PTZ in Screen and Joystick.

The PTZ control is only for the live views.

### 10.2.1 PTZ control with PTZ panel

Figure 53 PTZ Control Panel

① Select a Live view tab.

② Select a screen to control PTZ in the view.

③ Click the PTZ panel and click the operation button.

### 10.2.2 PTZ in screen

The PTZ in screen supports simple operations, panning, tilting and zoom.

① Select a Live view tab.

② Select a screen to control PTZ.

③ Click in the screen and drag to move.

④ Zoom is controlled by the mouse wheel operation.

* The length of the dragging line is the control speed.

Figure 54 PTZ in Screen

Figure 55 Zoom Control of PTZ in Screen

### 10.2.3 PTZ control with joysticks

* Connect the PC-compatible USB Joystick to the system. Some USB joystick devices need restarting the system to use.

① Select a Live view tab.

② Select a screen to control PTZ.

③ Move the stick.

④ There are predefined function buttons for control zoom, focus, iris and others.

Table 13 Joystick Buttons and PTZ Operations

| Buttons | Operations |
| --- | --- |
| 1 | Zoom Out (Wide) |
| 2 | Zoom In (Tele) |
| 3 | Focus Out (Far) |
| 4 | Focus In (Near) |
| 5 | Iris Out (Close) |
| 6 | Iris In (Open) |

## 10.3 Live Toolbar

Each view has view toolbar.

Figure 56 Live View Toolbar

### 10.3.1 View toolbar

The functions of each button in the toolbar are explained in ‘Appendix B - Toolbars’.

Click the Full screen button (), then the View mode would be changed as full screen mode. And if it is clicked in full screen mode, the toolbar would be disappeared. To show the toolbar in that mode, press the ‘ESC’ key. Then the toolbar is positioned on the top of the view. If you want to change the normal view mode as initial mode, close the full view screen by clicking the close button in the title bar or pressing Alt+F4 keys.

Table 14 View Toolbar

| Current view mode | Keys, Button | Transition mode |
| --- | --- | --- |
| Normal(Initial) view mode | Left Ctrl+Enter, | Full view mode |
| Full view mode | Left Ctrl+Enter, | Full view without toolbar |
| Full view mode | Left Alt+F4, | Normal view mode |
| Full view without toolbar | ESC | Full view mode |
| Full view without toolbar | Left Alt+F4, | Normal view mode |

### 10.3.2 Position

The toolbar is movable (top, left, right, bottom). Left click on the moving handle and dragging it.

Table 15 Toolbar Position

| Top |  |
| --- | --- |
| Left |  |
| Bottom |  |
| Right |  |

### 10.3.3 Screen title and toolbar

Each screen has the screen title. The title shows the channel name and current time.

An event is occurred, the background color of the title is blinked.

The channel/layout sequence mode the time displays with remaining dwell time.

The functions of each screen toolbar button are explained in the ‘Appendix B-Toolbars’.

Figure 57 Live Screen Title and Toolbar

1) Show and hide screen toolbar

Click the Show toolbar button () in the screen title. Then it would be changed to extended mode () and screen toolbar would be appeared.

If it is clicked with Left Shift Key pressing, all screen toolbars would be shown and hidden together.

2) Digital zoom control ()

Select the region to zoom by left mouse button clicking and dragging. The original screen would be shown in the right-bottom with PIP mode. And the zoom position is moving the region in the original screen. The zoom level is controlled by mouse wheel operation as the same way of PTZ in screen.

3) Snapshot ()

The snapshot button is to save the screen image with original size. If the automatic snapshot is enabled, the image file would be saved the configured directory. Otherwise, the file save dialog would be opened to select the file and directory. After saving the snapshot image file, the tooltip would be shown the filename.

If it is clicked with Left shift Key pressing, all channels are saved automatically with original size.

4) Disconnect ()

This is to close the screen. It is not the network disconnection but disconnection video/audio streams with the screen channel.

5) Freeze on/off ()

This is to stop the video and audio streams.

6) Speaker on/off ()

This is select audio stream.

* Please refer the device settings of audio. It is available only the case of that the device supports the audio transmission.

7) Microphone on/off ()

This is to transmit the audio stream to the device.

* Please refer the device settings of audio. It is available only the case of that the device supports bi-directional audio stream (audio-back channel).

8) Manual recording on/off ()

This is to start and stop recording manually. When a channel is not recording and the schedule for the device is not configured as recording time, if this is clicked, the video/audio streams would be recorded.

9) Show and hide text message ()

This is to show and hide text message. When it is set, device and user text messages would be displayed.

### 10.3.4 Screen exchange

Click the left mouse button in the screen title and drag it into other screen. Then the screens would be exchanged the position. If the exchanging channel is a sequence, then the sequence would be initialized. The exchanging screen is available with any live views (Live1, Live2, Emap and Event).

## 10.4 Event List

Click the Event tab beside of PTZ.

Figure 58 Event List

### 10.4.1 Event list

The Event list shows the real-time event information. If an event happened, it is listed with time, device name and event description and it would be highlighted.

Double-click the event item in the list or click the right mouse button and select the Open Live View from the menu. Then a window would be popped up and show the live video stream.

* The information in the Event list is not permanent.

* If the configuration is changed, the event information will be cleared.

* If the user logged out, the event list will be cleared.

* If the recording service is disconnected, the event list will be cleared.

* If the recording service records the data, the event information would be saved with video/audio. And the recorded events are able to be searched by the Event search in the playback.

Chapter 11 – Local Playback

This describes how to search and replay the recorded data (REC or HRA file). It supports various searching and replaying functions.

* HRA file is recorded via this software.

* REC file is recorded by camera on SD card in it.

## 11.1 Date and Time Search

The playback view supports a maximum of 16 channels.

Figure 59 Playback View

### 11.1.1 Date and time search

① Select the Playback tab and select the ‘Time lapse’ tab from the playback control tab.

② Select a device/group/layout item from the device tree.

③ Drag it into the view screen. If you drag a layout, then split mode will revert automatically as it is configured.

④ Select the date from the calendar. If there is any recorded data, the date will be highlighted in red

⑤ Select an hour item from the list. If there is any recording date, the number will be highlighted in red.

⑥ If the date and time is selected to replay, the time table will be shown with the recorded data information from each channel.

⑦ Select the time (minutes) to replay.

### 11.1.2 Device group and multiple devices

If a group is dragged into a screen in the playback view then the screens would be set as the order of the devices in that group.

For example, the group has 4 devices and the dragged screen number is CH 5, then the screen 5, 6, 7 and 8 would be set as the order of the devices in the group.

If multiple devices are dragged into a screen in playback view, then the screens would be set with the devices.

### 11.1.3 Layout

If a layout is dragged into a screen in the playback view then the screens would be set as the order of the devices in that layout. And the view would be changed as that layout.

## 11.2 Playback Controls

There are playback controls in the Timelaps tab.

### 11.2.1 Calendar and time combo-box

1) Calendar control

The calendar button () is to select the date. The calendar window shows the dates which have the recorded data or not as red.

Double click a date which has recorded data.

Figure 60 Playback Calendar Control

Table 16 Calendar Controls

|  | Previous Year |  | Next Month |
| --- | --- | --- | --- |
|  | Previous Month |  | Next Year |
|  | Today |  |

2) Time combo-box

Click the time combo-box. It shows 24 hours and the red color time means there is recorded data in that time. Select a time.

Figure 61 Time Combo-box

### 11.2.2 Export clip

Click the Export button () which is to save the footage as self-executable file. Select the date and time to be exported and format.

Figure 62 Remote Export

If you want to play clip-exe file before use password, check the “Use Password’ and input the password.

- Click Export clip button ().

- Select backup period using Date and time of Start and End.

- Select directory for backup.

- Select backup type. [ Normal( Exe file ) or AVI ]

- If user wants to backup with audio, click Audio check button ().

- Select camera channel for backup. [ All channel : click ALL CH check button() ]

- If user click Size button, backup size is displayed. [ Normal type backup displays size include viewer file ]

- To setup password for backup data, click Use Password check button ().

- When the password window is activated, type in password. [User needs to type in the correct password to view the backup image.]

- Click Export button.

### 11.2.3 Add favorite

Click the Add Favorite button () which is to add current playback time into favorite list.

And enter the favorite description.

The appended favorite is to be searched with the Favorite tab.

- Click Add favorite button.

- Type in information for adding favorite.

Figure 63 Insert Favorite

- User can search favorite information by clicking View Favorite button ().

### 11.2.4 Local file open

This button () is to open local HRA or REC file. Those files are made by this or recorded by the camera. The REC file MAY be made by a camera. And it MAY be exported the camera.

Click this button, then Local tab would be selected and a file open dialog would be popped up. Select a file to play (REC or HRA format).

### 11.2.5 Smart search

Currently not supported

### 11.2.6 Playback controls

1) Play speed control

This is to control the replaying speed. This speed control is applied only the Playing state.

The range is from x0.5 to x5.0. The speed is dependant on the system performance and load. The speed value x5.0 is not the meaning of accurate 5 times high-speed replaying.

Figure 64 Play Speed Control

2) Play controls

These are to control the playing mode. The backward playing controls show only key frames. The video encoding formats (MPEG4 and H.264) have Intra (key) frames. The image encoding format (MJPEG) has only Intra (key) frames. Thus in the case of backward playing of MJPEG, it shows all frames. But the others MAY be skipped.

The speed control is available only for the Forward playing mode.

The audio playing is available only for the Forward playing and x1.0 speed mode.

Table 17 Play Controls

| Buttons | Controls |
| --- | --- |
|  | Step backward playing with key frames |
|  | Backward playing with key frames |
|  | Forward playing with the speed control |
|  | Stop playing |
|  | Step forward playing |

3) Time jump

These are to jump with the specified time combo-box value. The available time jump range is from 5 to 30 seconds. Select the time from the combo-box and click the Time jump button. The playing mode (direction and state) would be kept. And the select time would be showed.

Table 18 Time Jump

| Buttons | Controls |
| --- | --- |
|  | Jump backward as the specified time |
|  | Jump forward as the specified time |

### 11.2.7 Time-overlapped playing

When the system time is changed, the recording system date and time MAY be overlapped. The time table shows which time is overlapped or not. And you can select the time overlapped recorded data.

The overlapped time period would be highlighted. Click the time, you can select the time id from the combo-box.

Figure 65 Time Overlapped Playing

## 11.3 Event Search

This is to search event data from the recording service and replay it.

Click the Event search button (). You can see the event search window.

Figure 66 Event Search

### 11.3.1 Event search ()

① Click the event search button from the playback control window.

② Select a device/group/layout item in the device tree.

③ Drag it into the view screen. If you drag a layout, then split mode will revert automatically as it is configured.

④ Select the search range using the start, end, date and time.

⑤ Select the event type to search from the event list. (If it isn’t selected anything, all events are searched.)

* The number of selected event items affects the length of the search time.

⑥ The result of the search event(s) will be displayed on the results page.

⑦ Select the event item to replay from the list and double-click it.

### 11.3.2 Clear ()

This is to clear all searched event list.

### 11.3.2 Export ()

This is to export event search result as CSV file format. The CSV file format is able to be opened with Microsoft Excel.

## 11.4 Favorite Search (Bookmark)

This is to search user favorite data.

Click the Event search button (). You can see the favorite search window.

Figure 67 Favorite Search

### 11.4.1 Favorite search

When you replay the recorded data in the Timelaps tab, you can add favorite by clicking the Add favorite button ().

Click the favorite button from the playback control window.

Select the search range using the start, end, date and time.

Enter the favorite text and click the search button.

The result of the favorite will be displayed on the results page.

Select the favorite item to replay from the list and double-click it.

### 11.4.2 Remove favorites

① Select the favorite item to modify.

② Click right mouse button and select the Remove menu.

### 11.4.3 Export favorites

This is to export favorite search result as CSV file format. The CSV file format is able to be opened with Microsoft Excel.

## 11.5 Event Report

This is to make the event report.

Click the Event Report button (). You can see the event search window.

Figure 68 Event Report

### 11.5.1 Make event report

① Click the event report button.

② Select the search range using the start, end, date and time.

③ Check the devices to make report from the Device combo-box.

④ Check the event types from the Event combo-box.

⑤ Click the Report button. The report result would be displayed as above.

The report shows how many times happened in that period with total event count.

### 11.5.2 Export event report

Click the Export button to export the Event report as CSV file format. This event report based the recorded data. If a stream was not recorded, then there is no event data to be reported.

## 11.6 Local File Playback

This is to replay the HRA and REC file which are stored in the local HDD.

Click the Local tab.

Figure 69 Local File Playback

### 11.6.1 Local file open

Click the File open button (). This is to open HRA or REC file format.

If there is any problem while opening the file, the message would be shown. While opening that file, it checks which has any file error or not.

The REC file is exported file from the network camera or device.

### 11.6.2 Export clip

This is to export clip from the original file.

Click the Export button () which is to save the footage as self-executable file or AVI format. Select the date and time to be exported and format.

Figure 70 Local Export

### 11.6.3 Time Bar

Time Bar shows time and date of Start and End for the video as well as the current position in the video.

Drag or click Thumb() to move desired position in time line.

Figure 71 Time Bar

### 11.6.4 Play controls

Please refer the ’10.2.6 Play controls’.

### 11.6.5 Event search

- Click local file open button() and select video data.

- Select search range using date and time of start and end.

- Select event type in the event list and click Search button. (At least one event type should be selected.)

* Search time depends on the number of selected items.

- User can find event search result in result page number and list.

- Select event item in the list and double click.

- The image moves to the start of the event.

### 11.6.6 Clear

Please refer the ’11.3.2 Clear’.

### 11.6.7 Export

Please refer the ’10.3.3 Export’.

## 11.7 Playback Toolbar

The Playback view has view toolbar. It’s similar with the ‘9.3 Live Toolbar’.

Figure 72 Local Playback Toolbar

### 11.7.1 View toolbar

The functions of each button in the toolbar are explained in ‘Appendix B - Toolbars’. And the full screen mode is the same with ‘9.3.1 View toolbar’.

### 11.7.2 Position

Please refer the ‘9.3.2 Position’.

The split bar of the Playback view is for resizing the view. Click the right mouse button and dragging, the playback view controls would be resized. Double click it, it would be minimized or restored the position.

Figure 73 Playback View Split Control

### 11.7.3 Screen title and toolbar

Please refer the ‘9.3.3 Screen title and toolbar’. The title shows the channel name and replaying time.

If an event was recorded in the replaying time, the background color of the title would be blinked. (This works only x0.5, x1.0, x2.0 playing speed and forward playing mode.)

The functions of each screen toolbar button are explained in the ‘Appendix B-Toolbars’.

Figure 74 Playback Screen Title and Toolbar

1) Show and hide screen toolbar

Click the Show toolbar button () in the screen title. Then it would be changed to extended mode () and screen toolbar would be appeared.

If it is clicked with Left Shift Key pressing, all screen toolbars would be shown and hidden together.

2) Digital zoom control ()

Select the region to zoom by left mouse button clicking and dragging. The original screen would be shown in the right-bottom with PIP mode. And the zoom position is moving the region in the original screen. The zoom level is controlled by mouse wheel operation as the same way of PTZ in screen.

3) Snapshot ()

The snapshot button is to save the screen image with original size. If the automatic snapshot is enabled, the image file would be saved the configured directory. Otherwise, the file save dialog would be opened to select the file and directory. After saving the snapshot image file, the tooltip would be shown the filename.

If it is clicked with Left shift Key pressing, all channels are saved automatically with original size.

4) Speaker on/off ()

This is to enable audio decoding and sound if there is audio data. This works only x0.5 playing speed and forward playing mode.

Chapter 12 – Device Playback

This describes how to search and replay the recorded data from External NVR/DVR devices.

Table 14 Function Support for NRV Type

|  | Hitron | Jupiter Plus / Venus NVR |
| --- | --- | --- |
| Device Type | NVR A | NVR B |
| Live | O | O |
| Event | O | O |
| PTZ | Up/Down/Left/Right | O | O |
|  | Diagonal | O | O |
|  | Magnify/Shrink | O | O |
|  | Focus | O | O |
|  | Iris | O | X |
|  | PAN Speed | O | X |
|  | TILT Speed | O | X |
|  | Preset & Save | O | O |
|  | Auto Scan | O | O |
|  | Tour | O | O |
|  | Pattern | O | O |
| Playback | Add favorite | O | O |
|  | Video Backup | O | O |
|  | Speed Control | O | O |
|  | Play Forward | O | O |
|  | Play Backward | O | O |
|  | Stop | O | O |
|  | Frame Back | O | O |
|  | Frame Advance | O | O |
|  | Time Jump | O | O |
| Search | Date & Time | O | O |
|  | Event | O | X |
|  | Favorite | X | X |
|  | Text-In | O | X |
| Setup | O | X |
| Recording | X | X |
| DDVRLS | X | O |

## 12.1 Device playback

Figure 75 Device Playback

The Device Playback view support a maximum of 16 channels. Device Playback support external NVR/DVR devices only.

### 12.1.1 Date and time search

Please refer the ‘10.1.1 – Date and time search’.

### 12.1.2 Device group and multiple devices

Please refer the ‘10.1.1 – Date and time search’.

### 12.1.1 Layout

Please refer the ‘10.1.1 – Date and time search’.

## 12.2 Playback Controls

Please refer to ’11.2 Playback Controls.

## 12.3 Event Search

Currently not supported.

## 12.4 favorite search

Please refer to ’11.4 Favorite Search.’

## 12.5 Text-In Search

Click the Show Text-In button (). You can see the Text-In search window.

The NVR maintains a log of each time the text-in data is detected. The Text-In Search screen displays this list. You can select the event for which you would like to see video.

Figure 76 Text-In Search

You can search video from the first to last recorded images, or you can set the start and stop times and dates.

Inactivating the First and Last box will allow the user to manually change the time to be searched.

Once you set your desired search conditions, click the   (   )    button to display the search results. Refer to “Appendix 5.6 Text-In Search” for more information.

Clicking an event list for which you would like to see video. The NVR will extract the event video and display the first image of the event. Pressing the PLAY,  button will start playing the “text-in” video segment.

You can see the detail text-in data by clicking ()  button to show pop-up window.

Figure 77 Text-In View

And also, you can click the ()    button to show the Filter Window.

Figure 78 Text-In Filter

1234567890123456789012345678901234567890123456789012345678901234567890

Item                   Price           Qty            amount

----------------------------------------------------------------------

Gillette Foamy     | $       10.1 |        1 | $            10.1

CD-RW              | $        5.1 |        1 | $             5.1

Coke               | $        2.2 |        2 | $             4.4

In the above text-in data, you can find that the comparison value is located at 21th (Price), 33th(Qty), and 45th(amount) characters (including spaces) from the left. In this case, you can enter “21”, “33” and “45” in each column box. For example, if you want to search for Gillete with a Price over $10 and CD-RW with an Qty of more than 1, the following search condition can be set.

## 12.6 Device Playback Toolbar

User can control playback view using Toolbar. This resembles  ‘10.3 Realtime View Toolbar’.

Figure 79 Device Playback Toolbar

- Toolbar

The functions of each button in the toolbar are explained in ‘Appendix B - Toolbars’.

Click the Full screen button (), then the View mode would be changed as full screen mode. And if it is clicked in full screen mode, the toolbar would be disappeared. To show the toolbar in that mode, press the ‘ESC’ key. Then the toolbar is positioned on the top of the view. If you want to change the normal view mode as initial mode, close the full view screen by clicking the close button in the title bar or pressing Alt+F4 keys.

- Position

Please refer the '11.7 (2) Position'.

- Screen Title and Toolbar

Each view window has screen title on top which shows the channel name and current time.

If event occurs, the background of the title blinks. (This works only in forward paly at x0.5, x1.0, x2.0 only.)

The functions of each button in the screen toolbar are explained in ‘Appendix B - Toolbars’.

Figure 80 Screen Title and Toolbar

- Screen Toolbar Show/Hide

Click the Show toolbar button () in the screen title. Then it would be changed to extended mode () and screen toolbar would be appeared.

If it is clicked with Left Shift Key pressing, all screen toolbars would be shown and hidden together.

- Digital Zoom Control ()

Select the region to zoom by left mouse button clicking and dragging. The original screen would be shown in the right-bottom with PIP mode. And the zoom position is moving the region in the original screen. The zoom level is controlled by mouse wheel operation as the same way of PTZ in screen.

- Image capture ()

The snapshot button is to save the screen image with original size. If the automatic snapshot is enabled, the image file would be saved the configured directory. Otherwise, the file save dialog would be opened to select the file and directory. After saving the snapshot image file, the tooltip would be shown the filename.

If it is clicked with Left shift Key pressing, all channels are saved automatically with original size.

- Disconnect ()

This is to close the screen. It is not the network disconnection but disconnection video/audio streams with the screen channel.

- Speaker on/off ()

This is select audio stream. (This function works only in forward playback at x1.0 speed.)

Chapter 13 – Emap View

This describes how to operate the Emap view and functions. It supports multi-layered Emap view. 36 maps are able to be loaded in the Emap View at the same time. Each map MAY have link(s) of other map(s) and sensor(s).

Figure 81 Emap View

## 13.1 Emap View

To design Emap, please refer the ‘3.6 System Setup – Emap’.

Click the Emap tab. The Emap view has all functions of Live1 except layout view. The layout view shows the Emap.

### 13.1.1 Emap and live view

1) Emap view

① Select a layout from the device tree.

② Click left mouse button and drag it into a screen in the Emap view.

③ If the map was designed for that layout, then the map would be shown. Otherwise, it shows default map background and devices.

2) Live view from map

① Select a device from the map.

② Click left mouse button and drag it into a screen in the Live1, Live2 and Emap view.

③ The screen would be set with the device and live stream would be shown.

④ You can select multiple devices by Left shift pressing and clicking the devices or dragging area in the map. The selected item would be highlighted.

### 13.1.2 Popup view

① Select a device or sensor from the map.

② Click right mouse button, select the Open Live View from the menu.

③ A window would be popped up and shows the live stream.

### 13.1.3 Manual trigger

① Select a sensor from the map.

② Click right mouse button. If it was designed as the Manual trigger button, select the Trigger from the menu.

③ You MAY check the operation from the Event tab or list.

### 13.1.4 Open link

① Select a link from the map.

② Double click it.

③ The map would be changed to the selected link.

④ Select a link from the map. Click left mouse button and drag it into a screen in the Emap view.

⑤ The map would be shown at the screen.

### 13.1.5 Event notification on a map

When an event is occurred, the device and sensor item would be blinked. And a layout link which includes that device or sensor would be blinked, too.

## 13.2 Emap Toolbar

The Emap view has view toolbar. It’s similar with the ‘9.3 Live Toolbar’.

Figure 82 Emap Toolbar

### 13.2.1 View toolbar

The functions of each button in the toolbar are explained in ‘Appendix B - Toolbars’.

And the full screen mode is the same with ‘9.3.1 View toolbar’.

### 13.2.2 Position

Please refer the ‘9.3.2 Position’.

### 13.2.3 Map controls

Map controls are available in the popup menu of a map. Click right mouse button on the background of a map. You can select menu from the popup menu.

1) Zoom

The background image would be zoomed in and out with these controls.

Table 19 Emap Zoom Controls

| Buttons | Controls |
| --- | --- |
|  | Zoom in |
|  | Zoom out |
|  | Fit screen on/off |

2) History of the links

You may open a link from the map. These are to move the history of the links in a map.

Table 20 Emap Zoom Controls

| Button | Control | Button | Control |
| --- | --- | --- | --- |
|  | Previous map |  | Next map |

3) Close

Select a map to close from the Emap view. Click the Close Emap button (). If you click this with Left Ctrl key pressing, then all maps would be closed.

4) Mouse move mode

Click right mouse button on the background of a map. Select the Mouse Move Mode from the popup menu.

This is to select mouse operation. If it is checked, mouse dragging is to move the map. Otherwise, it is to select the devices in the map.

Chapter 14 – Event View

This describes the Event view. The Event view has similar functions of the Live view. The different thing is that the event layout would be popped up automatically if the event is set. Please refer the ‘4.1 Event Setup – Device’.

Click the Event tab.

Figure 83 Event View

## 14.1 Event View

The Event view has the event screens and the event list. The event screens have similar functions of the Live except sequence controls, split controls and event channel setting.

You can drag devices, layout and sequences. The split mode is able to be controlled by the key pressing. Please refer the ‘Appendix D-Keys’.

If value of the event displaying dwell time is the Infinite, then the event layout would be shown continuously. But if the other event is occurred and it was set to show the other layout, then it would be switched. Even though the other event is occurred, if the displaying layout time is not over 5 seconds, it would not be switched. In that case, the event would be listed.

### 14.1.1 Toolbar control

Please refer the ‘9.3.1 View toolbar’ and ‘10.7.2 Position’.

### 14.1.2 Screen title and toolbar

Please refer the ‘9.3.3 Screen title and toolbar’.

## 14.2 Event Toolbar

There is no split mode and sequence controls in the Event view toolbar. The other functions are same with the Live view toolbar. Please refer the ‘9.3 Live toolbar’.

## 14.3 Event List

Please refer the ‘9.4 Event List’. This is the same with the Event list beside of the PTZ tab’. It shows event date and time, device and description.

Chapter 15 – Status View

The Status tab is to show device and system status and to get system/event log of devices.

Click the Status tab.

Figure 84 Status View

## 15.1 Status Toolbar

The status toolbar is to select status view mode.

Figure 85 Status Toolbar

There are view selection buttons and a full screen mode button.

This view doesn’t support the full screen mode without toolbar.

Table 21 Status Toolbar Buttons

| Buttons | Controls |
| --- | --- |
|  | Full Screen |
|  | Device Status and Live1, Live2 Layout |
|  | System Status and Monitoring/Recording Service Logs |
|  | Device System/Event Log View |

## 15.2 Device Status

The device status is to show the device connection, video and audio information and recording status. The Live1 and Live2 is to show what device is located in the view.

### 15.2.1 Device status table

Click the Device Status button () in the toolbar.

The Device status table shows the device status information. The device status would be updated in a few seconds. The updating period is dependant on the system performance. Thus it MAY be not correct in some time.

The frame rate and bit rate information is calculated by the recording service. It MAY be differ from the monitoring service.

Double click the device in the table, a window would be popped up and shows live stream.

Table 22 Device Status Table

| Column | Description |
| --- | --- |
| Name | Device Name and Connection Status |
| IP Address | Device IP Address |
| FPS (Rec) | FPS which recording service is receiving |
| BPS (Rec) | BPS which recording service is receiving |
| Resolution | Video Resolution (width x height) |
| Codec | Video and Audio codec |
| Recording | Recording Status |

Each row of device status table shows the connection status by the text color.

Table 23 Device Status Table Text Colors

| Field | Color | Description |
| --- | --- | --- |
| Name | White | Connected |
|  | Blue | Event |
|  | Red | Disconnected |
| Others | White | Recording |
|  | Gray | Not Recording |
|  | Red | Disconnected |

Figure 86 Device Status Table

### 15.2.2 Live1, Live2 split modes

The Device status view shows the split modes of Live1 and Live2 with assigned device name.

If you click the channel in the Live1 and Live2, the selected channel would be marked in split mode of the device status view.

If you click the channel in the split mode of the device status view, the channel would be selected in Live1 and Live2. And the channel would be highlighted in the status table.

Figure 87 Split Status

Double click the channel in the split status, then a window would be popped up and shows a live stream.

## 15.3 System Status

Click the System Status button () in the status toolbar.

It shows usages of the system resources and system logs.

Figure 88 System Status

### 15.3.1 Usages

The CPU, Network and Disk usages show the total CPU usages of the system which monitoring and recording services are running.

### 15.3.2 Monitoring and recording service logs

Figure 89 System Log Filter

1) Show current log

Select the Show Current Log from the combo-box.

It would clear the search results and shows system logs.

2) Log search

Select the searching range with start and end.

Select the Log type from the combo-box.

Click the Search button.

The logs would be searched and displayed. If the logs are more than 500, a page combo-box would be displayed to select.

The color of the log shows the log level, Operation, Critical, Warning and Error.

Click the column header (Date and time, Level, Operation, and Description), then the result would be sorted.

3)  Export

Click the Export button to export current displayed log as CSV file format.

Figure 90 Log Search Result

## 15.4 Device System/Event Logs

Click the Device System/Event Log button () in the toolbar.

This is to get and export device system and event logs.

Figure 91 Device System/Event Log

Select a device from the device tree which MUST be connected.

Click the System Log button or Event Log button.

The log from the device would be displayed in the viewer.

Click the Export button, it would be saved as TXT file format.

Chapter 16 – Clip Viewer

The Status tab is to show device and system status and to get system/event log of devices.

Click the Status tab.

Figure 92 Clip Viewer

## 16.1 Export Footage

You can save a part of original video clip. If you click Export Footage() button, you can save a part of the video clip in avi format by selecting date, time, file path, and channel.

Figure 93 Export Footage

## 16.2 Open Local File

This button() retrieves recorded HRA or REC files. If you click this button, an Open dialog box appears. Choose a file to play(REC or HRA format). File path for the recorded video has following type (Drive_name)\NCRecording\MacAddress\YYYYMMDDTTMMSS.hra.

## 16.3 Playback Control

- Play Speed ()

This function controls playback speed and applies only for playback. Playback speed can vary from x0.5 to x5.0 and actual speed depends on the system, so  x5.0 may not be 5 times the normal speed.

- Playback Control

Table 24 Playback Control

| Button | Function |
| --- | --- |
|  | Move To The Beginning |
|  | Step Backward (Key-frames only) |
|  | Backward Play (Key-frames only) |
|  | Play |
|  | Stop and initialize Channel Information |
|  | Step Forward |
|  | Move To The End |

- Time jump

This function enables time jump while playback of 5 to 30 seconds by selecting amount of time jump in combo-box and press Time jump(/ ) button. Playing mode(direction, speed) remains and time jumped video shall be displayed.

## 16.4 Event View

Figure 94 Event View

- Select a file you want to play at Open Local File() dialog box.

- Click Event View button ().

- Choose search range by selecting date and time of Start and End.

- Select event types from the event list and click Search button. (at least one event type should be selected)

- You can find the event you want to play on the event search result.

- Double click the event you want to play on the event search list.

- The channel for the event moves to the start moment of the event.

## 16.5 Split Mode()

Split Mode support 6 types of window split(). You select one of them and window changes to the selected one.

## 16.6 Snapshot

If you click Snapshot button () , Save As dialog box will appear and you select a path to save a snapshot image in bmp format.

## 16.7 Previous Split Group / Next Split Group

If you click an arrow(/), the window moves to previous / next split group.

Chapter 17 - Easy Install

Easy Install helps user to assign cameras on appropriate windows positions and to setup recording option heuristically. Click  button on top starts Easy Install.

* Easy Install works on 64 bits Hardware version only.

Figure 95 Easy Install

## 17.1 Easy Install procedure

- Click  button.

Figure 96 Easy Install – Setup

- Select a camera in right thumbnail list, drag & drop it to an appropriate channel window. Reload button refreshes camera thumbnail list.

- User can change camera arrangement by drag & drop of any two camera channels. Reset button clears all camera channels.

- After camera selection is completed, click Next button.

Figure 97 Easy Install – Camera Selection

- Select disk drives for recording and recording schedule.

* Disk drive should be 32GB or larger for recoding disk assignment.

Figure 98 Easy Install – Recording disk and schedule setup

- Click Apply button to finish Easy Install. [Previous button move back to Camera Selection.]

Chapter 18 - DDVRLS Setup

Titanium client can connect/view/control remote NVR in different network using DDVRLS function, which works only for Jupiter Plus / Venus NVR.

*  Both Titanium client and NVR must be connected to internet.

* If NVR is connect to internet via sharer, port forwarding should be set.(port number 9350)

Figure 99 DDVRLS Setup

## 18.1 NVR setup

- Network > ID, Password

- Type in ID / Password for Dashboard Setup, then click Register / Add button. If the registration is succeeded, “Success” shows on Dashboard Registration status.

Figure 100 Dashboard Setup Registration

- Type in ID / Password for DDVRLS, then click DDVRLS Register button. If the registration is succeeded, “Success” shows on DDVRLS Registration status.

Figure 101 DDVRLS Registration

- After setup type in the following address on web browser, http://h264viewer.com/dashboard. Log in using registered ID / Password for Dashboard Setup.

Figure 102 Dashboard Setup Login

- Remote Watch / Search button enables monitoring Live / Recorded video of NVR.

Figure 103 Remote Watch / Search

## 18.2 Titanium client setup

Figure 104 DDVRLS setup

- Main Menu > System Setup.

- Make a group in the tree and add a device manually.

- Once user select device type to “ NVR B”, DDVRLS setup items will show up.

- Change “Use DDVRLS” to True and  type in DDVRLS ID / PW used in NVR setup, then push Save button.

Appendix A - Specification

| Application/Version | NC-Titanium/1.0.0.0 |
| --- | --- |
| Recording |
| Number of Channels | 64 |
| Total Recording Bitrate | 128Mbps (32 x 4Mbps) |
| Resolution | 1080p, 720p, XGA, D1, VGA, QCIF, QVGA |
| Modes | Weekly Schedule, Special Day Schedule, Manual, Event-Relay |
| Special Day | 12 |
| Pre/Post-Recording | 60 sec/ 180 sec |
| Retention Time | 1 day ~ 1 Year |
| HDD | Internal/External HDD |
| Overwriting | Yes |
| Video/Audio | Yes (H264, MPEG4, MJPEG/G.711, G.726, PCM, AAC) |
| Live View |
| View Modes | Live1, Live2, Emap, Event, Popup |
| Split Modes | 4:3 mode,16:9 mode |
| Digital Zoom | Yes |
| PTZ | PTZ Panel, USB Joystick, PTZ in Screen |
| Audio | Yes (Multi-Selective Audio) |
| Channel/Layout Sequence | Yes (Unlimited) |
| Event View | Channel/Layout Popup and List View |
| Screen Exchange | Yes |
| Snapshot Mode | Automatic, Manual Save |
| Snapshot Format | BMP, JPEG, PNG |
| Aspect Ratio | Yes |
| Event Notification | Yes |
| Playback View |
| Channel | 16 |
| Date Time Search | Yes |
| Event Search | Yes |
| Text-In Search(Device Playback) | Yes |
| Time Jump | 5 ~ 30 sec |
| Play Speed | x0.5, x1.0, x2.0, x3.0, x4.0, x5.0 |
| Step Playing | Forward/Backward |
| Event Report | Bar Chart by Event Type |
| Split Modes | 4:3 mode(1, 4, 7, 9, 13, 16), 16:9 mode (12) |
| Event Notification | Yes |
| Local File Playback | Yes |
| Export Footage | Yes (Self-Executable/AVI) |
| Emap View |
| Configuration | Include (Camera/Sensor/Manual Trigger/Link) |
| Event Notification | Yes |
| Popup View | Yes |
| Multiple Emap | Yes (maximum 64 Emap on a screen) |
| Emap Control | Zoom/History List/Fit Screen |
| User Emap Image | Yes (Camera/Sensor/Manual Trigger/Link) |
| Event View |
| Device Event Actions | Recording/PTZ Move/Manual Trigger/Sound/ Run External Application/SMTP/Event Relay |
| Real-time Event Notification | Yes |
| Popup Live View | Channel/Layout with Dwell Time ( 5 sec ~ Unlimited) |
| Status View |
| Status Modes | Device Status/System Status/Device Log |
| Device Status | Live1/Live2 Layout mapped Status, Recording/Connection/Event Status |
| System Status | CPU/Network/Disk Usage, Real-time System Log, Log Search |
| System Log Search | Monitoring Service/Recording Service Log |
| Device Log | Yes |
| Log Export Format | Excel (csv), Text (txt) |
| Functions |
| Live Update | Yes |
| System Lock/Unlock | Yes |
| Automatic Login | Yes |
| Restoration | Yes |
| OSD Control | Yes |
| User Management | Yes |
| Authority Level | Administrator/User |
| User Assignment | Yes |
| Language | Export/Import |
| Video Output Mode | YV12/YUY2/RGB32/RGB565/RGB555 |
| Device Remote Setup | Yes |
| System Remote Setup | Yes |
| Device Searching Query | Yes |
| Device Discovery | Yes |
| Full Screen Mode | 2 Stages (Full Screen with/without Toolbar) |
| Hot keys | Split mode control/Split group control/Snapshot |

* Specifications are subject to change without notice

Appendix B - Toolbars

| Application/Version | NC-Titanium/1.0.0.0 |
| --- | --- |
| Live1/Live2 View |
|  | Wide 16:9 Split Mode (12, 20, 24) |
|  | Standard 4:3 Split Mode (1, 4, 7, 9, 13, 16, 21, 25, 33, 36) |
|  | Full Screen |
|  | Snapshot |
|  | Freeze |
|  | Manual Record Off/On |
|  | Speaker Mute On/Off |
|  | Microphone Mute On/Off |
|  | Disconnect All Devices |
|  | Previous Split Group |
|  | Next Split Group |
|  | Text Message Input |
|  | Set/Reset Event Channel |
|  | Sequence Mode Status/Off |
|  | Sequence Timer On/Off |
|  | Previous Sequence View Point |
|  | Next Sequence View Point |
|  | Sequence View Point List |
| Playback View |
|  | Wide 16:9 Split Mode (12) |
|  | Standard 4:3 Split Mode (1, 4, 7, 9, 13, 16) |
|  | Full Screen |
|  | Snapshot |
|  | Speaker Mute On/Off |
|  | Delete All Playback Devices |
| Emap View |
|  | Wide 16:9 Split Mode (12, 20, 24) |
|  | Standard 4:3 Split Mode (1, 4, 7, 9, 13, 16, 21, 25, 33, 36) |
|  | Full Screen |
|  | Snapshot |
|  | Freeze |
|  | Manual Record Off/On |
|  | Speaker Mute On/Off |
|  | Microphone Mute On/Off |
|  | Disconnect All Devices |
|  | Previous Split Group |
|  | Next Split Group |
|  | Text Message Input |
|  | Emap Zoom In |
|  | Emap Zoom Out |
|  | Emap Fit Screen |
|  | Previous Emap in History |
|  | Next Emap in History |
|  | Close Emap |
|  | Set/Reset Event Channel |
|  | Sequence Mode Status/Off |
|  | Sequence Timer On/Off |
|  | Previous Sequence View Point |
|  | Next Sequence View Point |
|  | Sequence View Point List |
| Event View |
|  | Full Screen |
|  | Snapshot |
|  | Freeze |
|  | Manual Record Off/On |
|  | Speaker Mute On/Off |
|  | Microphone Mute On/Off |
|  | Disconnect All Devices |
|  | Text Message Input |
| Status View |
|  | Full Screen |
|  | Device Status |
|  | System Status |
|  | Device System/Event Log |
| Screen Toolbar |
|  | Show/Hide Screen Toolbar |
|  | Move Left/Right Screen Toolbar |
|  | Digital Zoom |
|  | Screen Snapshot |
|  | Disconnect Channel |
|  | Freeze On/Off |
|  | Audio On/Off |
|  | Speaker On/Off |
|  | Manual Recording On/Off |
|  | Show/Hide Screen Text |

Appendix C - Directories

| C:\Program Data\NCTitanium (Windows 7) |
| --- |
| MonitoringService | Service configurations |
| Emap | Emap images and samples |
| Languages | Language ini files |
| Logs | Monitoring service logs and old configurations |
| Recording Service | Service configurations |
| Logs | Recording service logs |
| RecordingIndex | Recording data index |
| Users | User configurations |
| Shared | Common information |
| C:\Users\{User Name}\My Pictures |
| NCTitanium | Default snapshot directory |

Appendix D - Keys

| Live1, Live2, Event, Playback, Emap |
| --- |
| Page Up | Split Mode Changing (Decreasing Mode) |
| Page Down | Split Mode Changing (Increasing Mode) |
| Home | Split Group Changing (Circular Decreasing Mode) |
| End | Split Group Changing (Circular Increasing Mode) |
| Left Ctrl + Enter | Full Screen/Full Screen Without Toolbar |
| ESC | Full Screen Without Toolbar -> Full Screen with Toolbar |
| Left Alt + F4 | Close Full Screen Mode |
| Print Screen | Select Screen Snapshot |
| Left Shift + Print Screen | All Screens Snapshot |
| Left Ctrl + Emap Close Button | Close All Maps |

Appendix E - Messages and Logs

| Messages | How to do |
| --- | --- |
| OLE initialization failed. Make sure that the OLE libraries are the correct version. | Install Microsoft .Net framework |
| Windows sockets initialization failure. | Check and reinstall network device driver |
| Please check the storage space of the recording service. | Increase disk size in the system setup. Please refer the ‘3.4 System Setup – Disk’ - Overwriting failure or disk full. |
| The recording service is disconnected by another remote setup. Otherwise the service might be stopped. | The setup may be changed by the other system, it would be tried to reconnect automatically. Please check the service status in the system. |
| Please enter the user password. | User password is needed |
| The relaying stream is connected successfully | Recording service starts to relay live stream to monitoring system |
| No registered channel sequence group. Please add a channel sequence group. | Please add a channel sequence group. Please refer the ‘3.7 System Setup – Sequence’. |
| No registered layout sequence group. Please add a layout sequence group. | Please add a layout sequence group. Please refer the ‘3.7 System Setup – Sequence’. |
| Please enter a user ID. | Enter user ID |
| This user is already registered. | Try other user ID |
| Relay connection is failed. | Recording service fails to relay live stream. |
| There is no selected device. Please select a device. | Select a device from the device tree. |
| The updating version information file may have problem. It's not available. | The updating server is not accessible. Or the information file is not accessible. Please contact system administrator or installer |
| An error is occurred while getting the updating information file from the server. | Live updating information file is not accessible. Please contact system administrator or installer. |
| An error is occurred while getting and reading the version information file from the server. | Live updating version information file is not accessible. Please contact system administrator or installer. |
| An error is occurred while creating the updating file in the local disk drive. | File creation is failed. Please check the user authority and disk space. |
| An error is occurred while getting revision history file from the updating server. | Live updating revision history file is not accessible. Please contact system administrator or installer. |
| An error is occurred while getting the updating file from the server. Or it may be aborted. | The server might be disconnected while updating. Otherwise it was aborted. Try it again. And check the site. |
| No configuration server | Configuration may be corrupted. Otherwise check the recording service which is running or not. |
| There is no registered recording server. | Check the recording service which is running or not. Otherwise, the network firewall might be blocked to access. Please check the firewall of the system. |
| The monitoring service is being closed. | The monitoring service is being closed. Please wait until closed. |
| Deleting device playback information... | Please wait while handshaking of playback data and channel with the recording service. |
| This was terminated abnormally at the last time. Do you want to restore the last connection? | The last time the monitoring service was aborted or corrupted. |
| This file is not able to open. An error was occurred while opening this file. | Please try with other files. |
| An error is occurred while getting recording data. There may be no recorded data of the selected device(s). | Please check the recording status and recording disk drive and recording database. |
| Please set the correct searching time. The searching end time must be later than the start time. | Check the searching time range. |
| There is no selected event. Please select (an) event(s) from the list. | Check the event type from the combo-box. |
| An error was occurred while reading the Emap user image file. Please check the file and size. The image width must be multiply of 28 and the height must be 84. | Please refer the ‘3.6 System Setup – Emap’. |
| The CPU usage is more than 95%. The system may not work properly. | The CPU usage of monitoring system is more than 95%. The system may not work properly. Please check monitoring and playback devices and disconnect some of them. |

Appendix F – Hard Disk Format

Recording Server runs in background unless user stops operation, thus HDD format may cause damage in Recording Server while it is running. If user wants to format an HDD, please stop Recording Server before formatting as follows.

•

Hard Disk Format Procedure

- Start > All Programs > NCTitanium > Service Manager

Figure 104 Hard Disk Format - Service Manager

- Service Manager > select Recording Service and click right mouse button > Stop

Figure 105 Hard Disk Format - Service Manager Stop

- Format Hard Disk Drive

- Service Manager > select Recording Service and click right button > Start

Figure 106 Hard Disk Format – Service Manager Start

NC-Titanium

# Text boxes

NC-Titanium